## Slide 1: Design Space Exploration for Compressed Deep Convolutional Neural Network on SCALE Sim
Peilin Chen, Xinyuan Fu, Hanyuan Gao, Feilian Dai
6501 Group6
2024/12/05

## Slide 2
2024/12/3
2
The hardware platform we use
Systolic CNN AcceLErator Simulator (SCALE Sim)
Fig. Overview of SCALE Sim
https://github.com/scalesim-project/scale-sim-v2?tab=readme-ov-file
Samajdar, Ananda, et al. "A systematic methodology for characterizing scalability of dnn accelerators using scale-sim." 2020 IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS). IEEE, 2020.
SCALE Sim takes two files as input from the user: one is the hardware configuration, the other is the neural network topology (workload).
SCALE Sim generates two types of outputs: one is the cycle accurate traces for SRAM and DRAM, the other is the metrics like cycle counts, utilization, bandwidth requirements, total data movement, etc.

## Slide 3
2024/12/3
3
NN Quantization
LeNet-5 <-> Hand-written Digit Recognition
Fig. LeNet-5 Structure.
LeCun, Yann, et al. "Gradient-based learning applied to document recognition." Proceedings of the IEEE 86.11 (1998): 2278-2324.
LeNet-5:
three Convolutional layers, two Pooling layers, two Fully-connected layers.
Parameter size: C1(1×5×5×6+6) + C3(6×5×5×16+16) + C5(5×5×16×120+120) + F6(120×84) + OUTPUT(84×10) = 61,686

## Slide 4
2024/12/3
4
NN Quantization
Model definition
LeCun, Yann, et al. "Gradient-based learning applied to document recognition." Proceedings of the IEEE 86.11 (1998): 2278-2324.

## Slide 5
2024/12/3
5
NN Quantization
Linear asymmetric quantization
Linear quantization method:
Symmetric Quantization
Asymmetric Quantization
https://hanlab.mit.edu/courses/2023-fall-65940.
This part is useless.
Shortcoming
Asymmetric Quantization: Better than symmetric quantization because … But more complex.
Symmetric Quantization: Simple and easy to be implemented in hardware design. But it has a shortcoming.

## Slide 6
2024/12/3
6
NN Quantization
Training and Quantization results
Fig. train_loss & val_loss.
Fig. train_acc & val_acc.
The training and test batch size are 32 and 1000, respectively.
The learning rate and momentum are 0.001 and 0.9, respectively.
Compared to the original LeNet-5 model, the quantized int8 LeNet-5 model achieves no accuracy loss.
Fig. Original model vs. Quantized model.

## Slide 7
2024/12/3
7
Design Space Exploration
Design Space Exploration
Design Space Exploration
Definition: Given a network, optimize the hardware (Systolic Array) configuration (array size, dataflow)
Object: Performance (Cycles, the sim only provides the perf result)
Variable/Design Space: [Array Height, Array Width, Dataflow Type]
Scale-Sim
Perf
Result
Design Space
（Arraysize, Bufsize, Dataflow）
Hardware
Configuration
Software
Configuration

## Slide 8
2024/12/3
8
Design Space Exploration
Design Space Exploration
MLP
Scale-Sim
Perf
Result
Design Space
Hardware
Configuration
Software
Configuration
SAMPLES
Proxy Model
Hardware
Configuration
Software
Configuration
AI FOR AI HW!
For small space
Brute Force Search
For large design space,
the exploration time is huge (hours)
How to make it fast?
Search fast (Genetic, Simulated annealing …).
Estimate fast (A proxy estimator)
  Machine Learning
  Analytical Model (Timeloop, Maestro)
√
√

## Slide 9
2024/12/3
9
Design Space Exploration Result
Design Space Exploration Result
The accuracy is shown later.
Search (Single Layer Conv, PEs=64) Result
Time Cost Result
  Mins to < 1sec.

## Slide 10
2024/12/3
10
Proxy model
Why we need a proxy:
Motivation: SIM takes too much time,
Example: 500k design points cost 150+hours;
Why we choose MLP:
The task is a High-dimensional space function fitting task rather than a classification task;
MLP is a smooth model and a good fit for later searching;
MLP has a simple structure and we need a simple structure to prevent overfitting;
Parameters:
Width(systolic array)
Hight(systolic array)
Dataflow type(ws,os,is)
Buffersize
Software(mat mal)
    M,N,K(matrix)
Output is a number representing cycles
.
.
.
.
.
.
.
.
8 features input
Layer1
8x128
Layer2
128x256
Layer3
256x128
Layer4
128x64
Layer5
64x1
output
5 FC Layers MLP Network
MLP Network

## Slide 11
2024/12/3
11
Proxy model result
MLP Network
Our results:
Make batch size 1
Relative error within 1%
Fig. Prediction loss (MSE)
Fig. Relative prediction loss

## Slide 12: Thanks
THANKS